## Slide 1: Wheeled Locomotion
RBE500-F17-191
Lecture 07-2
Adj. Prof. Julian Center

## Slide 2: Locomotion of Wheeled Robots
Locomotion (Oxford Dict.):
Power of motion from place to place
Differential drive
Car drive (Ackerman steering)
Synchronous drive
Mecanum wheels
skid

## Slide 3: Instantaneous Center of Curvature
ICC
For rolling motion to occur without skidding, each wheel has to move only along its y-axis. Any x-axis motion is skidding. They all must move in a (generally) different radius about the Instantaneous Center of Curvature (ICC).

## Slide 4: Differential Drive
R
ICC
w
(x,y)
y
l/2
q
x
v
l
v
r
Sometimes we want to control with the robots forward velocity and the angular rate
But wheel controllers must use and

## Slide 5: Ackermann Steering
Your car has Ackermann steering so that the tires don’t skid on turns.
You also have a “differential” so that the outer tire can go faster then the inner tire because it must trace a larger circle.
ICC

## Slide 6: Simple Approximation for Designing Ackermann Steering
Invented by the German carriage builder Georg Lankensperger in Munich in 1817, then patented by his agent in England, Rudolph Ackermann (1764–1834) in 1818 for horse-drawn carriages.
Simple approximation for designing Ackermann linkage.
Source: Wikipedia

## Slide 7: Synchonous Drive
  q
y
x
v(t)
w( )
t

## Slide 8: Synchronous Drive Equations of Motion
  q
y
x
vi(t)
wi(t)
ICC

## Slide 9: Holonomic Drive with Mecanum Wheels
/4
Y
X
How to go sideways
Otherwise, drive is like tank drive.

## Slide 10: Dynamics of Mecanum Wheels
See Phidgets Holographic robot
https://www.youtube.com/watch?v=jxaSe6RJQvY
corresponds to spinning wheels but not moving

## Slide 11: Non-Holonomic Constraints
Non-holonomic constraints limit the possible incremental movements within the configuration space of the robot.
Robots with differential drive or synchro-drive move on a circular trajectory and cannot move sideways.
Holonomic robots, like those with Mecanum wheels, can move sideways.

## Slide 12: Holonomic vs. Non-Holonomic
Non-holonomic constraints reduce the control space with respect to the current configuration (e.g., moving sideways is impossible).
Holonomic constraints reduce the configuration space.
See Three Holonomic Robots
https://www.youtube.com/watch?v=_tmiu1wpp_E

## Slide 13: Calculating Planar Motion from Odometry Data

## Slide 14: Robot Motion
Robot motion is inherently uncertain.
How can we model this uncertainty?

## Slide 15: Probabilistic Motion Models
To implement the Bayes Filter, we need the transition model p(x| x’, u).
The term p(x| x’, u) specifies a posterior probability, that action u carries the robot from x’ to x.
In this section we will specify, how p(x| x’, u) can be modeled based on the motion equations.

## Slide 16: Coordinate Systems
In general the configuration of a robot can be described by six parameters.
Three-dimensional cartesian coordinates plus three Euler angles pitch, roll, and tilt.
Throughout this section, we consider robots operating on a planar surface.
The state space of such systems is three-dimensional (x,y,).

## Slide 17: Typical Motion Models
In practice, one often finds two types of motion models:
  Odometry-based
  Velocity-based (dead reckoning)
Odometry-based models are used when systems are equipped with wheel encoders.
Velocity-based models have to be applied when no wheel encoders are given.
They calculate the new pose based on the velocities and the time elapsed.

## Slide 18: Dead Reckoning
Derived from “deduced reckoning.”
Mathematical procedure for determining the present location of a vehicle.
Achieved by calculating the current pose of the vehicle based on its velocities and the time elapsed.

## Slide 19: Reasons for Motion Errors
bump
ideal case
different wheel diameters
carpet
and many more …

## Slide 20: Odometry Model
Robot moves from to .
Odometry information .

## Slide 21: The atan2 Function
Extends the inverse tangent and correctly copes with the signs of x and y.

## Slide 22: Noise Model for Odometry
The measured motion is given by the true motion corrupted with noise.

## Slide 23: Typical Distributions for Probabilistic Motion Models
Normal distribution
Triangular distribution

## Slide 24: Calculating the Error Probability (zero-centered)
For a normal distribution
For a triangular distribution
Algorithm prob_normal_distribution(a,b):
return
Algorithm prob_triangular_distribution(a,b):
return

## Slide 25: Calculating the Posterior Given x, x’, and u
Algorithm motion_model_odometry(x,x’,u)
return p1 · p2 · p3
odometry values (u)
values of interest (x,x’)

## Slide 26: Application
Repeated application of the sensor model for short movements.
Typical banana-shaped distributions obtained for 2d-projection of 3d posterior.
x’
u
p(x|u,x’)
u
x’

## Slide 27: Sample-based Density Representation

## Slide 28
Sample-based Density Representation

## Slide 29: How to Sample from Normal or Triangular Distributions?
Sampling from a normal distribution
Sampling from a triangular distribution
Algorithm sample_normal_distribution(b):
return
Algorithm sample_triangular_distribution(b):
return

## Slide 30: Normally Distributed Samples
106 samples

## Slide 31: For Triangular Distribution
103 samples
104 samples
106 samples
105 samples

## Slide 32: Rejection Sampling
Sampling from arbitrary distributions
Algorithm sample_distribution(f,b):
repeat
until ( )
return
Can be very inefficient!!!

## Slide 33: Sample Odometry Motion Model
Algorithm sample_motion_model(u, x):
Return
sample_normal_distribution

## Slide 34: Sampling from Our Motion Model
Start

## Slide 35: Examples (Odometry-Based)

## Slide 36: Velocity-Based Model

## Slide 37: Equation for the Velocity Model
Center of circle:
with

## Slide 38: Posterior Probability for Velocity Model

## Slide 39: Sampling from Velocity Model

## Slide 40: Examples (velocity based)

## Slide 41: Map-Consistent Motion Model

Approximation:

## Slide 42: Summary
We discussed motion models for odometry-based and velocity-based systems
We discussed ways to calculate the posterior probability p(x| x’, u).
We also described how to sample from p(x| x’, u).
Typically the calculations are done in fixed time intervals t.
In practice, the parameters of the models have to be learned.
We also discussed an extended motion model that takes the map into account.