## Slide 1: Perception in the Presence of Uncertainty II
Lecture 09-02
RBE500
Prof. J. Center

## Slide 2: Localization in a Mapped Environment

## Slide 3: Consider a Real Environment
85P as it was three years ago:

## Slide 4: Non-Parametric Localization
Replaces EKF or UKF by either Grid or Monte Carlo (Particle Filter) method.
Sensor models are essentially the same.
Grid methods use generally a fixed grid covering all possible states.
Particle filters can be scaled more easily.

## Slide 5: Advantages of Non-Parametric Methods over EKF and UKF
Can process raw sensor measurements.
  No need to extract features.
  Can process negative information
Able to handle a wide range of sensor and motion error distributions.
Can solve global Localization

## Slide 6: Grid Localization

## Slide 7: Creating a Grid in the State Space

## Slide 8: Grid Localization Approach
Establish a grid over the entire state space.
Use histogram filter methods.
  Fine grained grid is more accurate, but requires a large amount of computation.
  A course grid is inaccurate and presents problems for small movements or very accurate measurements.

## Slide 9: Grid Localization
Maintains a collection of discrete probability values.
Problems:
  Evaluating sensor data at a midpoint of course grid yields poor results.
  Slow motions in course grids lead to poor motion tracking.
Common Solution:
  “Fuzz up” the motion and sensor models.

## Slide 10: Grid Localization Computation
Evaluating at every grid cell is too computationally expensive.
Fixes:
  Precompute and cache motion and sensor models at all cells then do table look up.
  If prior localization is good enough, compute motion and sensor models only for local cells.
  Use lower frequency motion updates and selective sensor processing.

## Slide 11: Monte Carlo Localization

## Slide 12: Monte Carlo Localization
Most widely-used localization method.
Can solve global localization as well as tracking problems.
Uses particle filtering methods.
  Samples propagated through motion model. Then weighted by sensor model.
  New samples created by resampling.
  https://www.youtube.com/watch?v=H0G1yslM5rc

## Slide 13: General Monte Carlo Properties
Uses a large number of samples to model belief. Generally, the more the better.
Computations scale linearly with the number of particles.
Samples must be limited if motion or sensor models are expensive to compute. (Less and less a problem.)
Scan-base localization video

## Slide 14: Monte Carlo Localization Problems
Particle Starvation (Depletion) – Particles group together to soon around the wrong state.
Solved by adding additional randomly selected samples.
  Work backwards from current measurement to add points. Often not feasible because hard to compute.
  Add about 5% of random samples.
  “Fuzz up” sensor and motion models.

## Slide 15: Kullback-Leibler Divergence (KLD) Sampling
Adapts the number of samples as the more knowledge is gained.
Uses weighted samples without resampling
Uses a histogram to measure the spread of the samples.
Fairly complicated implementation. Justification depend on the problem.

## Slide 16: Localization in Dynamic Environments (1)
People are a problem!
Unexpected movement of objects present a problem.
Solution is to use a mixture model for sensor errors.
The mixture model for the sensor takes the form

## Slide 17: Beam-based Proximity Model
Measurement noise
zexp
zmax
0
Unexpected obstacles
zexp
zmax
0
The Problem!

## Slide 18: Beam-based Proximity Model
Random measurement
Max range
zexp
zmax
0
zexp
zmax
0

## Slide 19: Localization in Dynamic Environments (2)
The troublesome distribution is identified by estimating its coefficient, say , by
Assumes a Markov model.
If the probability of is above a threshold, we discard the measurement.

## Slide 20: Summary – Grid Localization
Grid methods use histograms to represent posteriors.
Grid coarseness trades off accuracy and computational efficiency.
For coarse grids it is usually necessary to “fuzz up” the motion and sensor models.
For fine grids, it may be necessary to update cells selectively.

## Slide 21: Summary – Monte Carlo Localization
Monte Carlo represents the posterior with a number of particles.
Adding random particles solves the “kidnapped robot” problem and mitigates particle depletion.
KLD-sampling varies the number of samples as knowledge is gains.
Environmental dynamics can be handled with mixture models.

## Slide 22: Beam Sensor Noise Models

## Slide 23: Assumptions for Range Sensors
The technique for determining this range is known as “ray tracing” or “ray casting.”
The idea is to mathematically extend a line from the sensor location to an object.
That forms a “range estimate” based on the assumed pose and the map (assumed available).

## Slide 24: Using Assumptions
Given a map, and an assumed position, we can calculate the expected ranges:

## Slide 25: Real Sensor Data
Let’s take some range measurements.
  ~3 Minutes, 100mS samples.

## Slide 26: A Closer Look – 0 to 30 Seconds

## Slide 27: Closer Look – 30 to 60 Seconds

## Slide 28: Closer Look – 60 to 130 Seconds

## Slide 29: Range Sensor Data
If the assumptions about pose are good, and the map is accurate, then this range is a good estimate.
  Otherwise it may be far off.
A sensor measurement made from the same location corresponds to the ray traced measurement.
  If the assumptions are good, they should be close.

## Slide 30: An Example
Consider a stationary platform:
  LIDAR range measurement.
  Known azimuth
    0 – 350 degrees10 degree increments
  Known initial location.
  “Known” map.

## Slide 31: The Mapped Environment – 85P

## Slide 32: The Test Setup

## Slide 33: The Real Environment

## Slide 34: Fundamental Error Sources
There are many sources of error:
  Sensors (of course!)
  What else?
Robot Pose
  How do we know the true location and orientation of the robot?
Map Errors
  plan != as built
  People, furniture, etc.

## Slide 35: Making Measurements
Whatever the pose is of the robot, measurements should approximate the environment.

## Slide 36: Good Assumptions
If the pose was a good estimate, the ray tracing and measurements should be consistent.

## Slide 37: Bad Assumptions
If the assumed pose was wrong, the error between measurements and calculations will be large (generally).

## Slide 38: Even Worse Assumptions
Of course, we may have rotation and translation:

## Slide 39: Localization
So, one way to perform localization would be to:
  Calculate the error between each ray traced point and the corresponding measurement.
  Rotate (and/or translate) the assumed platform location.
  Repeat until the overall error is minimized.
Symmetric environments, of course, would be a problem!

## Slide 40: Consider Robot Pose
First, we must acknowledge that we are working in multiple coordinate systems.
  The true map (if available) of our environment provides “world coordinates.”
  The robot platform itself provides “platform coordinates.”
  Making sense of platform data requires a transformation between coordinates.

## Slide 41: Robot and World
Let’s consider a simple case where the robot makes a range measurement to a wall:

## Slide 42: Robot and World
In the best of circumstances there will at least be sensor error.

## Slide 43: Robot and World
Generally there will also be error in the assumed location and pose.

## Slide 44: Reconciling Errors
A given sensor measurement is, essentially a conditional probability that is related to both the pose and the map.
For an assumed pose, and a map, the range between the robot and an object in the map can be calculated.

## Slide 45: Probabilities of Real Sensors
Assuming good sensors, maps, and reasonable pose assumptions, the expected relationship between world and sensor is:

## Slide 46: Unexpected Objects
Thus, with some probability, the measured range will fall short of the ray traced range

## Slide 47: Out of Range, Range Measurements
It is also possible, with probability, that an “infinite range” might be measured.

## Slide 48: And, of course, there’s noise…
Depending on the sensor, there may also be a random noise process that underlies the data:

## Slide 49: “Pseudo-density”
So, a real sensor, in a real environment, will typically contain a mixture of these random processes.
Mixture coefficients are used identify bad data.
We must quantify the components of the mixture model and their coefficients to get good localization.