## Slide 1: GPS NMEA Sentences
Source:
http://aprs.gids.nl/nmea/#bod

## Slide 2: GPS NMEA Sentences
$GPBOD - Bearing, origin to destination
$GPBWC - Bearing and distance to waypoint, great circle
$GPGGA - Global Positioning System Fix Data
$GPGLL - Geographic position, latitude / longitude
$GPGSA - GPS DOP and active satellites
$GPGSV - GPS Satellites in view
$GPHDT - Heading, True
$GPR00 - List of waypoints in currently active route
$GPRMA - Recommended minimum specific Loran-C data
$GPRMB - Recommended minimum navigation info
$GPRMC - Recommended minimum specific GPS/Transit data
$GPRTE - Routes
$GPTRF - Transit Fix Data
$GPSTN - Multiple Data ID
$GPVBW - Dual Ground / Water Speed
$GPVTG - Track made good and ground speed
$GPWPL - Waypoint location
$GPXTE - Cross-track error, Measured
$GPZDA - Date & Time

## Slide 3: $GPGGA Global Positioning System Fix Data
Name | Example Data | Description
Sentence Identifier | $GPGGA | Global Positioning System Fix Data
Time | 170834 | 17:08:34 Z
Latitude | 4124.8963, N | 41d 24.8963' N or 41d 24' 54" N
Longitude | 08151.6838, W | 81d 51.6838' W or 81d 51' 41" W
Fix Quality: - 0 = Invalid - 1 = GPS fix - 2 = DGPS fix | 1 | Data is from a GPS fix
Number of Satellites | 05 | 5 Satellites are in view
Horizontal Dilution of Precision (HDOP) | 1.5 | Relative accuracy of horizontal position
Altitude | 280.2, M | 280.2 meters above mean sea level
Height of geoid above WGS84 ellipsoid | -34.0, M | -34.0 meters
Time since last DGPS update | blank | No last update
DGPS reference station id | blank | No station id
Checksum | *75 | Used by program to check for transmission errors
Courtesy of Brian McClure, N8PQI.

## Slide 4: $GPGGA Global Positioning System Fix Data.
$GPGGA,hhmmss.ss,llll.ll,a,yyyyy.yy,a,x,xx,x.x,x.x,M,x.x,M,x.x,xxxx *cs
hhmmss.ss = UTC of position
llll.ll = latitude of position -- Two digits left of decimal are minutes of arc, right of decimal are fractional minutes, leading digits are degrees of arc. a = N or S
yyyyy.yy = Longitude of position -- Two digits left of decimal are minutes of arc, right of decimal are fractional minutes, leading digits are degrees of arc. a = E or W
x = GPS Quality indicator (0=no fix, 1=GPS fix, 2=Dif. GPS fix) xx = number of satellites in use x.x = horizontal dilution of precision x.x = Antenna altitude above mean-sea-level
M = units of antenna altitude, meters x.x = Geoidal separation M = units of geoidal separation, meters x.x = Age of Differential GPS data (seconds) xxxx = Differential reference station ID
cs = Checksum

## Slide 5: $GPGLL Geographic Position, Latitude / Longitude and time
$GPGLL,lll.ll,a,yyyyy.yy,a,hhmmss.ss,A*cs
llll.ll = Latitude of position -- The two digits left of decimal are minutes of arc, the digits to the right of the decimal are fractional minutes, the leading digits are degrees of arc
a = N or S
yyyyy.yy = Longitude of position -- The two digits left of decimal are minutes of arc, the digits to the right of the decimal are fractional minutes, the leading digits are degrees of arc a = E or W hhmmss.ss = UTC of position A = status: A = valid data
cs = Checksum

## Slide 6: $GPGSA GPS DOP and active satellites
eg1. $GPGSA,A,3,,,,,,16,18,,22,24,,,3.6,2.1,2.2*3C
eg2. $GPGSA,A,3,19,28,14,18,27,22,31,39,,,,,1.7,1.0,1.3*35 1 = Mode: M=Manual, forced to operate in 2D or 3D A=Automatic, 3D/2D
2 = Mode: 1=Fix not available 2=2D 3=3D
3-14 = IDs of SVs used in position fix (null for unused fields)
= PDOP
16 = HDOP
17 = VDOP
*
19-20 Checksum